## Slide 1: REED MULLER CODES ACHIEVE CAPACITY ON ERASURE CHANNELS S.Kudekar,S.Kumar,M.Mondelli,H.D.Pfister,E.Sasoglu,R.Urbanke
E2:207:Concentration Inequalities
Course Project Report
by
Ramakrishnan
Soumya Subhra Banerjee
ECE,IISc
December 2,2017

## Slide 2: Motivation
Another* answer to the search for PROVABLY capacity achieving channel codes.
Perhaps one of the most important applications of threshold phenomenon.
Establishes that a certain class of codes achieve capacity, Which include Reed-Muller codes,Polar codes.
*That polar codes achieve capacity was proved by E.Arikan before this.
This provides an alternate method of the same proof leveraging fewer properties of polar codes
The channel capacity is the largest rate at which communication can be made with arbitrary small error.
Channel coding tells us how capacity can be achieved.
Turbo , SC-LDPC achieve capacity, but no proof is presented yet
Polar and Reed-Muller were proved to achieve Capacity...

## Slide 3: Channel Capacity from the perspective of Threshold Phenomenon...proof idea
For transmission over BEC(p), with Capacity r=1-p
For a sequence of binary linear codes with rate r to be capacity achieving, the bit error probability,must converge to 0 for any erasure rate below 1 − r.
To prove this using Threshold Phenomenon.
Bit Error Probability for a code , under MAP decoding needs to be captured by a function of erasure probability.We shall explore MAP EXIT (Extrinsic Information Transfer) functions for this.
MAP EXIT function should be expressed as measure of a monotone set
The influences of the set must be equal , in other words ,the set must be symmetric.This happens when we assume the code is 2-transitive under automorphic permutation.
Hence we will apply Russo's lemma.
The critical value will occur at p=1-r, this follows, from Area theorem
RM codes , Polar codes are 2-transitive.

## Slide 4: Bit Map Decoding under BEC
Decoding rule
Bit error Probability
Observation 1, Bit error probability = Transinformation:
, ,if Xi is Ber(1/2).
Proof:
if Xi can be recovered from
Else ,
=p

## Slide 5: MAP EXIT functions...to capture bit error probability
Definition:
the vector EXIT function associated with bit i,
the average EXIT function,
we can choose pi=p for all i.
Implication:
It is the Transinformation associated with each bit 'i',which comes from all bits of received vector except bit 'i' (hence the name EXtrinsic Information Transfer)
Observation 2,Bit error probability vs EXIT function:
By definition of conditional Entropy...
Further using Observation 1,

## Slide 6: MAP EXIT function ...area theorem
Propostion 1*.
The MAP EXIT function satisfies ...
Proof:
noting that the second term is independent of pi, and differentiating gives the above result.
* Note the propositions are numbered according to original paper

## Slide 7: MAP EXIT function ...area theorem
Proposition 4(c), Area Theorem:
The area under average EXIT function is equal to the rate
Implication:
This theorem will govern where the threshold will lie.
Proof:
from proposition 1,
this implies, for a parameterized vector, , t Є(0,1)
consider pi(t)=t
noting, , , ,,and using the definition of h(p) completes the proof.

## Slide 8: MAP EXIT function ...as a measure of a set
Consider bit erasure pattern a as a indicator vector s.t. ai=1{ Yi=e}
A binary vector a covers another vector c if ai > ci, for all i.
A transmitted codeword can be recovered iff the erasure pattern does not cover any codeword.
A bit i can be recovered uniquely iff the error pattern does not cover any codeword where bit i is non-zero.
 | 1 | 2 | 3 | 4 | 5 | 6 | E does not cover
E | 1 | 0 | 0 | 1 | 0 | 0 | 
C1 | 1 | 0 | 1 | 1 | 1 | 0 | True
C2 | 1 | 1 | 0 | 1 | 0 | 1 | True
C3 | 1 | 0 | 0 | 1 | 0 | 0 | True
C4 | 1 | 0 | 0 | 0 | 0 | 0 | X

## Slide 9: MAP EXIT function ...as a measure of a set
Indirect Recovery:Consider a code C and the indirect recovery of Xi from the subvector Y∼i (i.e., the bit-MAP decoding of Yi from Y when Yi = e).
For i ∈ [N], the set of erasure patterns that prevent indirect recovery of Xi under bit-MAP decoding is given by,
Intuitively, it is the set of all erasure patterns, that cover some codeword with bit 'i' = 1, if 'i' is included.hence strengthens
Proposition 3(a),4(a), hi(p) is measure of Ωi :

## Slide 10: MAP EXIT function ...as a measure of a set
Proof:
by definition of conditional entropy,
WOLOG assume all 0's were sent.due to error pattern A , few bits got erased.
thus,
Now , if A ∈ Ωi , then decoding fails hence , ,else 0.
thus,
the result follows on considering, pl=p.

## Slide 11: MAP EXIT function ...Influences of Ωi
Ωi
flip j
flip j
The measure of this set is the j-th influence of Ωi

## Slide 12: MAP EXIT function ...Influences of Ωi
We need to show next :
all influences are equal, hence the set is symmetric ...
all hi(p) are equal , hence area theorem can be applied...
these will stem from the assumption that the code is 2-transitive
Proposition 3(b),4(b), jth partial derivative of hi(p) is jth influence of Ωi :
Proof: similar to proposition 3(a),4(a)

## Slide 13: Permutation group...briefing
Symmetric group SN of [N]:
Is the set of all permutations of N possible.
[N=3] , SN={{1,2,3},{1,3,2},{2,1,3}...}
Permutation group is a subset of symmetric group.
C
π
Considering [N] denotes the set of indices of a code a permutation operation(π) is a rearrangement of the bits of a code.
A Permutation automorphic group PAut(C) of a code is the permutation group , suchthat under π ∈ PAut(C) the membership of the code is preserved, we denote PAut(C), as

## Slide 14: Permutation group...transitivity
if for any , there exists,
, such that
then is transitive.
C
π
code with bit 'b' at index i
code with bit 'b' at index j
if for any , there exists,
, such that,
then is doubly-transitive.
C
π
code with bit 'b' at index i, bit 'c' at index k.
code with bit 'b' at index i, bit 'c' at index j.

## Slide 15: MAP EXIT function ...for doubly transitive code
Proposition 7, All EXIT functions are equal , for a transitive code:
i.e,using,

## Slide 16: MAP EXIT function ...symmetry
Proposition 8, All Influences are equal , for a transitive code:
for distinct,
Proof:
Similar to Proposition 7.Intuitively we expect that once we permute the
locations , the bits which were pivotal must continue to remain so.Otherwise we could
have decoded the concerned bit using simple permutations.

## Slide 17: Outline...
EXIT function
Area theorem,connection to rate
Measure of a monotone* set
Influences of the set
2-Transitivity of code
Symmetry
Russo's lemma and Threshold phenomenon
Equivalence of Capacity to threshold phenomenon of EXIT function
Probability of bit error
Applicability of Area theorem
2-transitive codes are Capacity achieving
Reed Muller/polar codes are capacity achieving
partial derivatives

## Slide 18: Capacity achieving codes...equivalence
The following are equivalent,
S1: {Cn } is capacity achieving on the BEC under bit-MAP decoding.
S2: The sequence of average EXIT functions satisfies
S3: For any,
note,
While S1 S2 , follows from relationship between hi(p) and probability of bit error ,the rest follow from area theorem
Suppose {Cn} is a sequence of codes with rates {rn} where rn → r for
r ∈ (0, 1). a) {Cn} is said to be capacity achieving on the BEC under bit-MAP decoding, if for any p ∈ [0, 1 − r), the average bit-erasure probabilities satisfy,

## Slide 19: Capacity achieving codes...
The average EXIT function of Rate-1/2 RM-code with,Block length N.
Shows threshold phenomenon.

## Slide 20: Main result...threshold phenomenon
Influence:
for a Monotone set Ω, the j-th influence is defined as.
the total, Influence is defined as,
Theorem 19:Let Ω be a monotone set and suppose that, for all the influences of all bits are equal ,i.e,
Then, for any
where pt = inf{p ∈ [0, 1] : μp(Ω) > t} is well defined because μp(Ω) is strictly increasing in p with μ0(Ω) = 0 and μ1(Ω) = 1.
Proof: follows from Russo's lemma

## Slide 21: Main result...notations
Redefinitions
We can redefine Ωi as a set of indicator vectors of A.
Accordingly ,we can refine the definition of the measure...

## Slide 22: Main result...
This implies,
Hence , and Cn achieves Capacity.
Properties of Ωi'
Ωi' is the set of error patterns that prevent the detection of Xi.
Consider A ∈ Ωi' , any B > A will surely cause error.Hence B ∈ Ωi' and thus,
Ωi' is monotone.
Recall,
hence, thus Ωi' is symmetric.
Let {Cn} be a sequence of codes where the blocklengths satisfy Nn → ∞, the rates satisfy rn → r, and the permutation group G(n)(of Cn) is doubly transitive for each n. If r ∈ (0, 1), then {Cn } is capacity achieving on the BEC under bit-MAP decoding.
Proof:
Note, , , where h(n)(p) is the EXIT function of Cn.

## Slide 23: Polar codes are Capacity achieving... Introduction to polar codes
Channel polarization is an operation by which one manufactures out of N independent copies of a given B-DMC W,a second set of N channels {W(i)N : 1 ≤ i ≤ N } that show a polarization effect in the sense that, as N becomes large,the symmetric capacity terms {I(W(i)N )} tend towards 0 or 1,for all but a vanishing fraction of indices i. This operation consists of a channel combining and a channel splitting phase.

## Slide 24: Polar codes are Capacity achieving... polar codes are doubly - transitive ,hence achieve capacity
Proof:
Assume we are given four distinct locations in the code a,b,c and d ∈ [N] ,we need to give a permutation π : [N] → [N] such that,
π(a) = c and π(b) = d , and it is automorphic.
Consider any permutation which satisfies the above constraint,proving it is automorphic suffices.
Note , πN×N ∗ [u1 ...un ] = [u π(1) ...u π(n) ]
and, πN×N ∗ [x1 ...xn ] = [xπ(1) ...xπ(n) ]
Hence,upon premultiplying the encoding equation with π ,we get
π ∗ [x1 ...xn ] = π ∗ [u1 ...un ] ∗ Gn
⇒ [xπ(1) ...xπ(n) ]=[u π(1) ...u π(n) ] ∗ Gn
As polar codes are linear , and [u π(1) ...u π(n) ] is a valid message, so [xπ(1) ...xπ(n) ] is a
valid codeword too.hence proved

## Slide 25
Thanks...